## Slide 1: AP Environmental Science
Air Pollution (Chapter 16)

## Slide 2: History of Air Pollution
1550 – first observation of photochemical smog
17th century- first observation of acid rain
18th century- recognition of smog and acid rain as damaging to plants
1905- introduction of “smog” as a technical term
1948- Donora Zinc Works air pollution event
1952- London smog crisis
1997 & 2015- Indonesian wildfires

## Slide 3: History of Air Pollution
South Asian Brown Cloud
Brown smog cloud 2 miles thick
Directly linked to 380,000 deaths per year
Contributes to 40% crop losses
Circulation of pollution by prevailing winds travels around the globe in 2 weeks
Effects in the U.S. = 25% increase in particulate matter, 77% increase in carbon soot, 33% increase in mercury pollution

## Slide 4: History of Air Pollution
The atmosphere has a short residence time making it a convenient place for waste disposal that results in pollution (movement of air pollution video)
Following the Donora and London events air control became a major issue
  Clean Air Act of 1955
Legislation to reduce air pollution emissions has been successful but chronic exposures to air pollutants continues to contribute to illness and death worldwide
Current health care systems struggle to keep up with the demands caused by environmental related health issues

## Slide 5: History of Air Pollution
Currently the EPA maintains a list of 188 hazardous air pollutants (HAPs) that it is required to control (complete list)
Each year industries that produce more than 25,000 pounds or handles more than 10,000 pounds of a toxic chemical must provide a report to the Toxic Release Inventory
  667 chemicals must be reported
An Air Quality Index is generated to inform the public of daily threats to their air quality based on measurable pollutants and local reports (AirNow website)

## Slide 6: Sources of Air Pollution
Stationary sources
Point sources emit pollutants from one or more controllable sites.
Fugitive sources generate air pollutants from open areas exposed to wind processes.
Area sources are well defined areas within which are several sources of air pollutants

## Slide 7: Sources of Air Pollution
Mobile sources
Move from place to place while emitting pollutants (vehicles)
Natural sources
Particulate emissions from natural processes (volcanic eruptions, wildfires, lightning)

## Slide 8: Sources of Air Pollution

## Slide 9: Effects of Air Pollution
Discoloration of the atmosphere resulting in reduced visual range and clarity
Damage to plants
  Tissue damage, suppression of growth, susceptibility to environmental conditions, disruption of reproductive processes
Damage to animals
  Toxicity, cancer, birth defects, eye and respiratory irritation, susceptibility to infection and heart disease, chronic diseases

## Slide 10: Effects of Air Pollution
Healthy people may be able to acclimate to pollutants so that they feel like they have no symptoms even though the pollutants may continue to affect them
Many air pollutants have a synergistic effect where they combine to have greater effects than the individual pollutant would on its own
The respiratory system in vertebrate animals is affected more than any other body system
(TED talk on the global pandemic from air pollution)

## Slide 11: Effects of Air Pollution

## Slide 12: Types of Pollutants
Air pollutants occur either
in gaseous form or as small
liquid or solid materials called
particulate matter
Two Types:
Primary pollutants emitted directly into the air
Secondary pollutants created through reactions between primary pollutants and other compounds in the air
Chart: 
| CO | VOC | NO | SO | Particulates
Primary Pollutants | 0.58 | 0.11 | 0.15 | 0.13 | 0.03

## Slide 13: Types of Pollutants

## Slide 15: Types of Pollutants
Secondary pollutant reactions require a collision between molecules which occurs rarely because of the relatively low density of the atmosphere.
Most atmospheric reactions that occur require a free radical.
Free radicals are produced from stable molecules being broken apart (typically through photolysis) to form atoms that have unpaired electrons. These atoms are much more reactive than the original molecule.

## Slide 16: Types of Pollutants
Hydroxyl (OH) is one of the most important atmospheric radicals formed from the photolysis of tropospheric ozone
OH is short lived and almost immediately reacts with compounds like carbon monoxide, methane and VOCs

## Slide 17: Types of Pollutants

## Slide 18: Types of Pollutants
Sulfur Dioxide (SO2)
Colorless odorless gas
Once emitted can be converted to sulfateSO4
Removed from atmosphere by wet or dry deposition
Major human sources; coal power plants, industrial processes
Adverse effects depend on dose and concentration present
  Injury or death to animals and plants
  Corrosion of paint and metals
  Important precursor to acid rain

## Slide 19: Types of Pollutants
Nitrogen Oxides
Occur in many forms in the atmosphere but largely emitted in two forms:
  Nitrogen monoxide - NO
  Nitrogen dioxide - NO2
    A yellow-brown to reddish-brown gas
    May be converted to NO31-
  Both subject to emissions regulation and contribute to smog
  NO2 major contributor to acid rain

## Slide 20: Types of Pollutants
Nitrogen Oxides
Nearly all NO2 emitted is from human sources
  Automobiles and power plants that burn fossil fuels
Environmental effects:
  Irritate eyes and mucous membranes
  Suppress plant growth
    However when convert to nitrate may promote plant growth

## Slide 21: Types of Pollutants
Carbon Monoxide
CO is a colorless, odorless gas
  Even at low concentrations is extremely toxic to humans
    Binds to hemoglobin in blood.
  90% of CO in atmosphere comes from natural sources
  10% comes from fires, cars, and incomplete burning of organic compounds

## Slide 22: Types of Pollutants
Ozone and other Photochemical Oxidants
Photochemical oxidants result from atmospheric interactions of nitrogen dioxide and sunlight.
  Most common is ozone (O3)
  Colorless gas with slightly sweet odor
  Very active chemically, oxidizes or burns
    Beneficial in the upper atmosphere
  Hard to regulate
Effects include
  Kills leaf tissue at high concentration
  Damage eyes and respiratory system
  Even young, healthy people may have breathing difficulty on polluted days

## Slide 23: Types of Pollutants
Particulate Matter
PM10 is made up of particles less than 10μm in diameter
  Present everywhere but high concentrations and/or specific types dangerous
  Much particulate matter easily visible as smoke, soot, or dust
  Includes airborne asbestos and heavy metals
Of particular concern are very fine pollutants
  PM2.5- less than 2.5 μm in diameter
  Easily inhaled into the lungs, then absorbed into the bloodstream
  Ultrafine particles- <0.18 μm released by automobiles.
    Related to heart disease

## Slide 24: Types of Pollutants

## Slide 25: Types of Pollutants
Particulate Matter
When measured often referred to as total suspended particles (TSPs)
  Tend to be highest in large cities in developing countries
Recent studies estimate that 2 to 9% of human mortality in cites is associated with PM
  Linked to both lung cancer and bronchitis
  Especially hazardous to elderly and those with asthma
Dust can be deposited on plants
  Interferes w/ absorption of CO2 and O2 and transpiration
Block sunlight and may cause climate change

## Slide 27: Types of Pollutants
Lead
A constituent of auto batteries and used to be added to gasoline.
  Lead in gas emitted into air with exhaust
  Spread widely around world in soils and water along roadways
  Once in soil can enter the food chain
  Lead now removed from gas in US, CAN, EU
    98% reduction in emissions since 1970s

## Slide 28: Additional Pollutants
Hydrogen Sulfide
Highly toxic corrosive gas easily identified by its rotten egg odor.
Produced from
  Natural sources such as geysers, swamps, and bogs
  Human sources such as industrial plants that produce petroleum or that smelt metals.
Effects of hydrogen sulfide include
  Functional damage to plants
  Health problems ranging from toxicity to death for humans and other animals.

## Slide 29: Additional Pollutants
Hydrogen Fluoride
Extremely toxic gaseous pollutant
Released by some industrial activities
  Such as production of aluminum, coal gasification, and burning of coal in power plants.
Even a small concentration (as low as 1 ppb) of HF may cause problems for plants and animals.
  Potentially dangerous to grazing animals because forage plants can become toxic when exposed to this gas.

## Slide 30: Additional Pollutants
Methyl Isocyanate (CH₃NCO)
An ingredient of a common pesticide
  known in the United States as Sevin.
Colorless gas
Causes severe irritation (burns on contact) to eyes, nose, throat, and lungs.
  Breathing the gas in concentrations of only a few ppm causes violent coughing, swelling of the lungs, bleeding, and death.
  Less exposure can cause a variety of problems, including loss of sight.

## Slide 31: Additional Pollutants
Methyl Bromide (CH₃Br)
Colorless, odorless, nonflammable gas
Ozone depleting chemical
Used as a pesticide (strawberries, tomatoes)
Produced naturally and artificially
  Naturally by marine organisms and some plants
Undergoes photolysis to create bromide that destroys stratospheric ozone

## Slide 32: Additional Pollutants
Volatile Organic Compounds
Variety of organic compounds used as solvents in industrial processes
  Dry cleaning, degreasing, and graphic arts.
Hydrocarbons
  Comprise one group of VOCs.
  Thousands of hydrocarbon compounds exist, including natural gas, or methane (CH4); butane (C4H10); and propane (C3H8).
Some VOCs react w/ sunlight to produce photochemical smog
Globally 15% of hydrocarbons emissions are anthropogenic
  In the US 50%
  Primary human source automobiles

## Slide 33: Additional Pollutants
Benzene
Additive in gasoline and an important industrial solvent.
Produced when gasoline and coal undergo incomplete combustion.
  Also component of cigarette smoke
  Major environmental source on and off road vehicles

## Slide 34: Additional Pollutants
Acrolein
A volatile hydrocarbon that is extremely irritating to nose, eyes, and respiratory system.
Produced from
  Manufacturing processes that involve combustion of petroleum fuels
  Component of cigarette smoke

## Slide 35: Variability of Air Pollution
Problems vary in different regions of the country and the world.
  LA pollution mainly from mobile sources
  Ohio and Great Lakes point sources
Also varies with time of year
  Smog a problem in summer when there is lots of sunshine
  Particulates a problem in dry months

## Slide 36: Urban Air Pollution
Whether air pollution develops depends on topography and meteorological conditions
  Determine the rate at which pollutants are transported away and converted to harmless compounds.
In the lower atmosphere, restricted circulation is associated with inversion layers may lead to pollution events.
Atmospheric inversion
occurs when warmer
air is found above cooler
air

## Slide 37
Primarily summer and fall conditions
Increased cloud cover creates stagnant air

## Slide 38: Urban Air Pollution
Potential for urban pollution is determined by the following factors:
  Rate of emission of pollutants per unit area.
  Downwind distance that a mass of air moves through an urban area.
  Average speed of the wind.
  Elevation to which potential pollutants can be thoroughly mixed by naturally moving air in the lower atmosphere.

## Slide 39: Urban Air Pollution
Concentration of pollutants in the air is directly proportional to the first two factors.
  As either emission rate or down wind travel distance increase, so will the concentration of pollutants
City air pollution decreases w/ increases in third and forth factors.
  The stronger the wind and the higher the mixing layer, the lower the pollution.

## Slide 41: Urban Air Pollution
Smog
Two major types
  Photochemical smog (LA type smog or brown air)
  Sulfurous smog (London type smog, gray air, or industrial smog)
Photochemical smog reaction involves sunlight, nitric oxides and VOCs
  Directly related to automobile use
Sulfurous smog is produced by the burning of coal or oil at large power plants.

## Slide 44: Future Trends
As we understand more about where air pollution is coming from we should be able to improve air quality
Steps to improve air quality include:
  Reduce emissions
  Improve transportation
  Stricter regulations on pollutant sources
Developing countries face more difficulty controlling air pollution because of a lack of infrastructure around industry and urban environments

## Slide 45: Pollution Control
The most reasonable strategies for control have been to reduce, collect, capture, or retain the pollutants before they enter the atmosphere.
  Reduction of emissions through energy efficiency and conservation measures is preferred.
Implementing pollution control must be a social, political, economical and global priority to be truly effective

## Slide 46: Pollution Control
Sulfur Dioxide Control Techniques
Washing- allowing iron sulfide to settle out of a solution (does not get sulfur combined with carbonaceous compounds)
Coal gasification- converts coal to gas to remove sulfur (expensive)
Scrubbing- Sulfur dioxide released during coal burning is sent through a slurry of lime (CaO) and water which causes the sulfur to react with calcium and precipitate out
Liquid ammonia- reacts with sulfur to create ammonium sulfate which can be cooled and collected in condensing towers

## Slide 47: Pollution Control

## Slide 48: Air Pollution Legislation and Standards
Clean Air Act Amendments of 1990
  Goal to reduce coal burning emissions by 50% by 2000 (achieved)
  Incentives to reduce emissions including permits that allow companies to buy and sell the right to pollute
  Reduce nitrogen dioxides (auto emissions)
  Reduce toxic air emissions by 90%
  End productions of all CFCs by 2030

## Slide 49
Kyoto Protocol (1997)
Main goals were to control emissions that contribute to increases in greenhouse gases and human induced climate change
Established emissions trading policies (cap and trade) that would help to regulate emissions from countries and individual industries within countries
Places more responsibility on developed countries due to their historical influence on greenhouse gases

## Slide 50: Air Pollution Legislation and Standards
Clean Power Plan of 2015
Plan to reduce carbon emissions from power plants (70% reduction by2030)
Focuses on states regulating and reducing carbon emissions
Promotes accountability from industries by requiring plans to reduce emissions by 2016
Invests in clean energy options and job creation
Hopes to reduce energy costs for the average household

## Slide 51: Air Pollution Legislation and Standards
Air quality standards study the levels of certain pollutants that could be hazardous to health
Requires tougher standards for PM2.5 and ozone
Increases monitoring of emissions by the EPA
Sets the Air Quality Index for common pollutants

## Slide 52: Air Pollution Legislation and Standards

## Slide 53: Costs of Air Pollution Control
Costs for pollution control vary with the types of industry
Goals are to balance the cost of clean up with the benefits
Could require taxing citizens for pollution emissions
Should focus on the cost of health care in the future because of environmental toxins

## Slide 54: Sulfur Dioxide Effects

## Slide 55: Nitrogen Dioxide or Carbon Monoxide Effects

## Slide 56: Ozone Effects