## Slide 1: Ap environmental
Fossil fuels and the environment (ch.19)

## Slide 2: Fossil fuels
Fossil fuels still supply approximately 80% of the World’s commercial energy
Fossil fuel use is declining due to climate change concerns and the rapidly growing renewable energy sector but the United States and many other countries still have a heavy dependence on fossil fuels that will likely continue for many decades

## Slide 3: Fossil fuels
Forms of stored solar energy (converted into chemical energy by photosynthesis)
Result of incomplete biological decomposition
Stored in sedimentary rocks

## Slide 4: Coal
Solid, brittle, carbonaceous rock
  Most abundant fossil fuel
  Found mostly in North America, Europe and Asia with proven reserves mostly in China, Russia, and the United States
Classified according to its energy and sulfur content
  Anthracite
  Bituminous
  Subbituminous
  Lignite
Energy content greatest in anthracite and lowest in lignite
Lower sulfur coal emits less sulfur dioxide

## Slide 5: Coal

## Slide 6: Coal concerns
Coal can be mined from the surface through strip mining or mountain top removal or from underground shafts
  Mining for coal is dangerous for workers and leads to environmental concerns
Mountain top removal
Strip Mining

## Slide 7: Coal concerns
Burning coal emits harmful pollutants
  Sulfur dioxide, nitrogen oxides and carbon dioxide are released in the process of burning coal
  Additional toxins such as mercury, arsenic, chromium, lead, and uranium could be released into the air from coal impurities
  Coal power plants emit more radioactivity into the surrounding environment than nuclear power plants
Coal combustion produces toxic ash that must be stored on sites around power plants and can be vulnerable to spills into surrounding ecosystems

## Slide 8: Coal
Coal combustion is the greatest environmental concern.
Legislation worldwide has restricted the amount of pollutants produced by coal burning plants but not enough to prevent damage to the environment and cause climate shifts
As oil and gas reserves dry up more pressure is put on coal.
Increased use of coal will have significant environmental impact due to the increase in pollutants.

## Slide 9: Coal
Options for cleaner coal include:
  Physical cleaning before combustion
  Injection of material rich in calcium carbonate into the gases following burning (scrubbers)
  Conversion of coal at power plants into gas before burning.
  Convert coal to oil.
  Carbon capture and storage in rock beds
  Goal: Development of zero emissions coal-burning electric power plants

## Slide 10: Crude oil and natural gas
Generally believed to have formed from organic materials buried with aquatic sediment beds in depositional basins
Most are found along geologically young plate boundaries or faults but can be formed away from plate boundaries as well
Source material is fine grained organic sediment buried at least 500 meters below the surface under increased heat and pressure

## Slide 11: Crude oil and natural gas

## Slide 12: Crude oil and natural gas
Elevated pressure causes sediment to be compressed which initiates upward migration to lower-pressure reservoir rock
Reservoir rock is coarser grained and relatively porous
  E.g. sandstone and porous limestone
Natural upward migration of the oil and gas is interrupted or blocked in a trap
  Rock that helps form a trap is known as cap rock, often shale

## Slide 13: Crude oil and natural gas
Anticline Trap
Fault Trap

## Slide 14: Petroleum production
Primary production
  Involves simply pumping the oil from wells
  Recovers only 25% of petroleum in reservoir
Enhanced recovery
  Increase the amount recovered to about 60%
  Steam, water, or chemicals injected into the reservoir to push oil towards wells

## Slide 15: Petroleum Production
Next to water, oil is the most abundant fluid in the upper crust
  Concentrated in a few fields
  Proven reserves of oil are a part of the total resource that can be extracted for profit
  65% of oil reserves are found in 1% of fields, mostly in the Middle East
  Total resource numbers have been increasing with better technology to identify depositional basins
  Increases in proven oil reserves have only come from discoveries in some of the largest oil fields (Middle East, Venezuela, Kazakhstan)

## Slide 16: Petroleum production

## Slide 17: Oil in the 21st century
Recent estimates of proven oil reserves suggest that oil and natural gas will last only a few decades.
When will we reach peak production?
  Likely to have already passed meaning people alive today will have to adjust to potential changes in lifestyle and economies in a post-petroleum era
We are approaching the time when approximately 50% of the total crude oil available from transitional oil fields will have been consumed.
Proven reserves are about 1.2 trillion barrels. World consumption is quickly using what is left.

## Slide 18: Oil in the 21st century
Measurement of future resource availability is the reserves-to-production ratio calculated by dividing the volume of total proved reserves by the volume of current annual consumption
  Over time global oil reserves will may increase as new technologies will be able to increase production and access oil not currently profitable for extraction
  Currently, for every three barrels of oil we consume, we are finding only one barrel
  In the US production of oil as we know it now may end by 2090. World production by 2100.

## Slide 19: Oil Concerns
Drilling technology and the exploration of oil deposits in the arctic and deep ocean have increased the threat of environmental damage from spills
Recent discovery of oil in Canada’s tar sands has led to clearing of vast amounts of boreal forest and the construction of additional pipelines through North America
Geopolitical volatility and economics have also led to an unstable market for oil

## Slide 20: Oil concerns
Oil refineries take crude oil and through a process of distillation turn the oil into various products
Refineries release volatile organic compound pollutants into the air that are dangerous for ecosystems and humans

## Slide 21: Oil Shale
Fine grained sedimentary rock containing organic matter mixtures (kerogen).
  Not the same as crude oil or tight oil but can be used as a substitute called synfuel
  More expensive to extract and process
  When heated to a high temperature pyrolysis occurs that turns oil shale into a vapor that can be turned into a usable form of oil
  Examples of oil-bearing shales are the Marcellus Shale, Bakken Formation, Pierre Shale, Niobrara Formation, and Eagle Ford Formation.

## Slide 22: Oil Shale

## Slide 23: Tar Sands
Sedimentary rocks or sands impregnated with tar oil, asphalt, or bitumen.
  Recovered by mining the sands and then washing the oil out with hot water.
  Most abundant reserves located in Alberta, Canada
  Strip mined in large swampy areas that are deforested, drained, and then removed layer by layer

## Slide 24: Tar Sands

## Slide 25: Natural Gas
Only begun to utilize this resource
  Transported by pipelines, not able to be safely shipped long distances
Currently makes up ¼ of the global energy consumption
Considered a clean fuel
  Produces fewer pollutants (specifically sulfur oxides) than burning oil or coal
  Could be a transition fuel to alternative energy

## Slide 26: Natural Gas
The main compound in natural gas is methane that naturally accumulates as coal and oil is broken down
Most natural gas reserves are found in the Middle East and Russia but gas trapped in tight sand and shale deposits have been identified in the United States

## Slide 27: Natural Gas
Natural gas sources
  Crude oil wells with a gas cap above the crude oil trap or gas dissolved in the oil produce associated gas
  Gas wells and condensate wells are gas sources that contain little to no crude oil and are called non-associated gas
  Condensate wells that contain heavier forms of natural gas (pentane) can also produce low weight hydrocarbons in the gas product

## Slide 28: Natural gas

## Slide 29: Natural Gas
Fracking is the process of drilling down into the earth before a high-pressure water mixture is directed at the rock to release the gas inside.
  Water, sand and chemicals are injected into the rock at high pressure which allows the gas to flow out to the head of the well.

## Slide 30: Natural Gas

## Slide 31: Natural Gas Concerns
Water consumption and contamination from fracking
Cheap prices inhibits the market exploration of energy from renewable energy sources
Intercontinental shipping of natural gas is dangerous due to the volatility of the gas and the possibility of ignition

## Slide 32: Methane Hydrates
Beneath the seafloor there exist deposits known as methane hydrates
  White, ice like compound made up of molecules of methane gas molecular “cages” of frozen water
  Forms as a result of microbial decomposition on the sea floor and then trapped in ice
  Also found on land in permafrost
Found in ocean where deep, cold seawater provides high pressure and low temperatures.
  Not stable at lower pressure and warmer temps.
Potential energy source but currently no way to mine or transport the gas

## Slide 33: Methane Hydrates
Recent releases of methane hydrates have been documented in the Arctic ocean and in the permafrost of Russia